PI3HDX511E

Demo Board Rev.A User Manual
by Ada Yip

Table of Contents

1	Introduction	2

2	Overview	2

3	Quick Start	3

4	Circuit Description	4

4.1	Equalization Setting	4

4.2	Swing and Pre-emphasis Settings	4

4.3	Source Termination Setting	4

4.4	Output DDC Pull-up	5

4.5	5V Power Supply	6

4.6	Power Saving Mode	6

5	References	6

6	Appendix A: Demo Board Schematic	7

# Introduction

PI3HDX511E HDMI1.4 re-driver is designed for source applications. This user manual describes the components and the usage of PI3HDX511E Demo Board Rev.A.

# Overview

Figure 1 is the block diagram of Pericom PI3HDX511E demo board and figure 2 shows the top view of the demo board. One HDMI plug connector (J101) on PI3HDX511E demo board is used for plugging a source device, such as a DVD player. An HDMI cable can be connected between an HDMI receptacle connector (J102) on the demo board and a sink device, such as HDTV. +5V DC can be employed to the demo board via a mini USB female connector (J103) and/or the source device provided that a header pin JP105 is shorted. Through a 3.3V regulator (U102), PI3HDX511E on the demo board can then be powered up.

For source application evaluation, SCL and SDA are pulled to 5V at output HDMI connector through shorting header pins JP103-4. Swing, pre-emphasis and equalization settings of PI3HDX511E can be adjusted via a SPDT switch (SW101).

Figure 1: Block Diagram of PI3HDX511E Demo Board Rev.A

Figure 2: Top View of PI3HDX511E Demo Board Rev.A

# Quick Start

To start-up the PI3HDX511E demo board Rev.A, complete the following steps:

- Short header pins JP103-4 to pull DDC signals to 5V at output HDMI connector side;

- Open all the switches on SW101 to enable PI3HDX511E, set 5dB equalization, set 500mV swing, set 1.5dB pre-emphasis, and enable source termination;

- Short JP105 to allow employing a 5V DC to the demo board from a source device;

- Supply 5V to demo board from mini USB connector at J103;

- Plug HDMI input connector at J101 to a source device, e.g. DVD player;

- Connect a sink device, e.g. HDTV, to HDMI output connector at J102 using an HDMI cable.

# Circuit Description

# Equalization Setting

PI3HDX511E offers three equalization settings for source application. Setting below is for referencing.

| EQ_S0 | Equalization | Pins 5 and 12 of SW101 Pins 6 and 11 of SW101 | Input FR4 Trace (in) or Input HDMI Cable (m) |
| --- | --- | --- | --- |
| 0 | 2.5dB | Short pins 6 and 11 | 2” – 6” |
| Float or VDD/2 | 5dB | All open | 4” – 16” |
| 1 | 7.5dB | Short pins 5 and 12 | 12” – 24” |

Table 1: EQ Setting of PI3HDX511E Demo Board Rev.A for Source Application

Figure 3: SW101 on PI3HDX511E Demo Board Rev.A

# Swing and Pre-emphasis Settings

Swing and pre-emphasis settings of PI3HDX511E are designated for fulfilling source eye diagram requirement specified in HDMI specification. Swing is desired as 500mV while three pre-emphasis settings can be picked depending on individual PCB design.

| OC_S0 | Swing | Pre-emphasis | Pins 3 and 14 of SW101 Pins 4 and 13 of SW101 | Output Trace |
| --- | --- | --- | --- | --- |
| 0 | 500 mV | 0dB | Short pins 4 and 13 | 1” – 2” |
| Float or VDD/2 | 500 mV | 1.5dB | All open | 2” – 8” |
| 1 | 500 mV | 2.5dB | Short pins 3 and 14 | 6” – 16” |

Table 2: OC Setting of PI3HDX511E Demo Board Rev.A for Source Application

# Source Termination Setting

Source termination embedded in PI3HDX511E is used to minimize the reflection due to any impedance mismatch before PI3HDX511E. For any transmission higher than 2.2Gbps, source termination is recommended.

| ROUT_S0 | Pins 2 and 7 of SW101 | Source Termination |
| --- | --- | --- |
| 0 | Short | Disabled |
| 1 | Open | Enabled |

Table 3: Source Termination Setting of PI3HDX511E Demo Board Rev.A

# Output DDC Pull-up

Per HDMI specification, DDC lines are required to be pulled to 5V for source application. To evaluate PI3HDX511E in source application, headers JP103-4 are shorted so as to pull SCL and SDA to 5V via 2.2kΩ resistors at output HDMI connector.

Figure 4: DDC Pull-up at Output HDMI Connector of PI3HDX511E Demo Board Rev.A

47kΩ pull-up resistors are also reserved for DDC lines at input HDMI connector of PI3HDX511E demo board Rev.A. These two resistors may be needed for cable evaluation. The resistors can pull SCL and SDA to 5V by shorting headers JP101-2.

Figure 5: DDC Pull-up at Input HDMI Connector of PI3HDX511E Demo Board Rev.A

# 5V Power Supply

By shorting header JP105, PI3HDX511E demo board Rev.A can be powered up through two methods. 5V can be employed from:

- any source connected to input HDMI connector J101 via +5V_A power rail;

- Mini-USB adaptor connected to mini USB2.0 connector J103 via +5V_USB power rail.

Figure 6: Power Circuit of PI3HDX511E Demo Board Rev.A

# Power Saving Mode

PI3HDX511E can enter power saving mode by setting /OE pin to high voltage level.

| /OE | Pins 1 and 8 of SW101 | Output TMDS of PI3HDX511E |
| --- | --- | --- |
| L | Short | Normal Mode |
| H | Open | Power Saving Mode |

Table 4: /OE Setting of PI3HDX511E Demo Board Rev.A

PI3HDX511E also offers automatic output squelch feature and HPD detection. If no input clock signal is present and/or HPD sink is at low level, PI3HDX511E will shut down TMDS output to enter sleep mode for power saving.

# References

- High-Definition Multimedia Interface Specification Version 1.4b, HDMI Licensing, LLC, October 11, 2011

- High-Definition Multimedia Interface Compliance Test Specification Version 1.4a, HDMI Licensing, LLC, March 4, 2010

# Appendix A: Demo Board Schematic

For clearer view of schematic diagram, please click the PDF file icon on the right.

# Text boxes

PI3HDX511E

J102

3.3V Regulator

Mini USB Connector

Input Port

U102

SW101

SPDT Switch

J101

HDMI Input Connector

HDMI Output Connector

Output Port

U101

+5V_A

J103

+5V_USB

+3V3

Short

Short

Short